## Slide 1
GLIOLIGHT – VINS modeling attempts
From singlet-oxygen signals to oxygen dynamics, light transport and PDT/DLT modelling
Aleksandra Maluckov
Modelling-status talk:
what has been tried,
what physics we clarified,
what must still be constrained before quantitative PDT/DLT prediction.
1

## Slide 2
Main modelling tasks
Fitting provides the target.
Modelling asks which physical state could have produced it.
2
We need a forward model that mimics the measurement process.
1 Reproduce S(t)
Generate the measured photon-counting curve from sample physics, not only from a fit function.
2 Oxygen dynamics
Model oxygen supply, respiration and light-induced consumption in monolayers and spheroids.
3 Light → chemistry
Connect the local optical field to PpIX excitation or to an effective PS-free ROS source.
4 Synthesis
Use a virtual experiment to generate a measured-like curve.

## Slide 3
What is common and what is different between PDT and DLT?
3
PDT: 5-ALA / PpIX-assisted branch
• 5-ALA → PpIX inside cells
• light excites PpIX → triplet PS
• triplet PS transfers energy to ground-state O₂
• source depends on I(r), PpIX(r), O₂(r,T)
• bleaching can matter
DLT / PS-free branch
• no added PpIX / photosensitizer branch
• light is mapped to an effective ROS / ¹O₂-like source
• optical propagation can be simulated
• conversion efficiency is not independently fixed
• this is the open physical part
Key message: the general modelling architecture can be similar, while the chemistry connecting light to the source term is different.
PDT is the reference; DLT is the branch requiring additional physical calibration.

## Slide 4
1. First modelling attempts
This is the map of what has actually been tried and what each part clarified.
4
Monolayer / thin samples
processed 1270-nm curves; gas–liquid O₂ supply; simpler first optical path
Spheroids
radial O₂ diffusion; respiration and PDT sink; local O₂ changes kinetics
Virtual experiment
freeze slow profiles; calculate fast kinetics; generate synthetic S(t)
Mouse / in vivo next
first measurements started; tissue optics and perfusion; model to be formulated
The purpose of these simpler models is to understand which physical quantitates really control the observable.

## Slide 5
2. Oxygen dynamics module
Slow sample state: oxygen supply competes with respiration and light-induced consumption.
5
Main state variable*: Cₒ₂(r,T) = local molecular oxygen concentration on seconds/minutes time scale (T)
∂Cₒ₂/∂T = diffusion − respiration − light-induced oxygen sink
oxygen enters and
spreads through the sample
cells consume oxygen biologically
PDT/ROS chemistry can consume oxygen
Monolayer  oxygen supply from the medium is presented by an interface flux
J(O₂) = Kᴸ (Csat − Csurface)
KL - mass transfer coefficient at the interface, not the internal diffusion coefficient.
Spheroid  oxygen has to diffuse to the center being continuously consumed
O₂ gradients and a hypoxic core
*State- slow state variables: spatial oxygen and photosensitizer distributions, Cₒ₂(r,T) and CPS(r,T) , cell bleaching state
So radius, respiration, external oxygen and illumination all matter before we even start discussing the microsecond luminescence signal.

## Slide 6
Oxygen depletion and triplet kinetics
Connection between oxygen transport and the measured kinetics.
1. Oxygen depletion estimate in spheroid sample
Ccenter ≈ Cext − q R² / (6D)
larger R or q → stronger O₂ depletion larger D → better O₂ replenishment
→
2. Oxygen is also quenching channel of PpIX triplet
1 / τT(r) = 1 / τT,0 + kq CO₂(r)
O₂ ↓ → weaker triplet quenching → local τT increases
What the detector fits
A spheroid contains many local τT(r) values. The detector sees the spatially summed emission, so the fitted τT is an effective value, , not one microscopic lifetime.
Key message: The first equation tells us whether oxygen depletion is expected; the second tells us how this depletion can appear in the kinetics.
to the measured
lifetime
6

## Slide 7
Spheroid example:
Layered spheroid model
Outer shells: better oxygen supply
Inner shells: lower oxygen
O2 in
r
Each shell i is assigned a local oxygen level Ci(T). Then a local microsecond signal Si(t) is computed and spatially summed.
Measured curve and fitted response
NCH82 spheroid - Blue dots: measured time-resolved 1270-nm signal. Orange line: fitted phenomenological curve.
What was extracted / what the model gave
Experimental fit (selected spheroid)
A = 278.47 =8.47 μs = 1.57μs Aphos = 70, BG = 0, χ ≈ 1.11
First oxygen-to-signal bridge
C(r,T) → τT(r,T) → Slocal(r,t) → Stotal(t) Central O2: 0.2000 → 0.1898 atm = 7.7 μs
= 1.05 μs
Main message: at this stage the trend is meaningful lower oxygen gives weaker triplet quenching and therefore a longer effective triplet-related lifetime.
+BG
7

## Slide 8
ŝ · ∇L(r,ŝ) = −(μa + μs)L(r,ŝ)+ μs ∫ p(ŝ,ŝ′) L(r,ŝ′) dΩ′ + Sopt(r,ŝ)
L(r,ŝ): radiance — light at position r travelling in direction ŝ Sopt: laser/source term injected into the optical problem μa, μs: absorption and scattering coefficients p(ŝ,ŝ′): scattering phase function
Physical starting point: radiative transfer
3. Optical module: from light transport to the local source term
The optical calculation should provide the absorbed-light field used by the oxygen / ROS model.
Output of optics
Φ(r) = ∫₄π L(r,ŝ) dΩ
fluence rate: local optical power from all directions
→
Qabs(r) = μa(r) Φ(r)
absorbed optical power density
→
qPDT(r) or qDLT(r)
source / sink term for the next model
Sopt creates the light field; Qabs = μaΦ is the absorbed field that drives the local PDT/DLT chemistry.
What chemistry needs
Model input
s = − ln(ξ) / (μa + μs)
s- sampled free path between photon interactions
Each photon is followed through the real geometry: absorption, scattering, interfaces, beam profile,top / bottom illumination and wavelength-dependent coefficients.
Practical implementation: Monte Carlo photon transport
The interface between the optical model and our oxygen-photochemistry model is well defined: a spatial optical field, with known wavelength, geometry and normalization.
8

## Slide 9
WHERE PDT and DLT SEPARATE AFTER THE OPTICAL CALCULATIONS
9
PDT branch — physically clearer
I₆₃₅(r) + CPpIX(r,T) → triplet PS → ¹O₂
• 5-ALA/PpIX pathway gives a constrained photochemical chain
• local source depends on optical field, PpIX and oxygen
• PDT is the reference branch for testing the model architecture
DLT / PS-free branch — open source law
I₁₂₆₇(r) → ? → effective ROS / ¹O₂ source
• no added PpIX / triplet mediator
• optical field can be calculated, but conversion efficiency is not fixed
• the DLT source term must be measured, bounded or calibrated
Downstream from that source term, however, the oxygen and signal modelling steps can be shared.

## Slide 10
4. Virtual experiment: putting the pieces together
10
slow time T
seconds / minutes
optical pulse
one excitation event
microtime t
0–80 μs after trigger
1. Slow sample state
Oxygen, photosensitizer and cells evolve during treatment. This is transport / biology time, not microsecond fitting time.
∂Cₒ₂/∂T = diffusion − respiration − light sink
2. Freeze + illuminate
At one treatment time T*, the slow profiles are frozen.
One optical pulse sees local values in each shell or voxel.
Cᵢ = Cₒ₂(rᵢ,T*) Qabs(r) from optics → local excitation
3. Fast photophysics and signal
After the pulse, triplet population decays, singlet-oxygen is produced and decays and photons are emitted.
triplet PTᵢ(t) → singlet Δᵢ(t) →Svirtual(t)
dPTᵢ/dt = −(k₄ + kq Cᵢ)P Tᵢ
dΔᵢ/dt = ΦΔ kq Cᵢ P Tᵢ− kΔ Δᵢ
Svirtual(t) =Σi Wi[kradΔ Δi + kphos P Tᵢ]
Detector-like synthetic signal: Smeasured(t) = IRF * Svirtual(t) + BG. Fitting procedure gives effective observables A, , ,Aphos.
In other words: first we generate the measurement, and only then we fit it.

## Slide 11
5. Current status and next step
The model is useful as a transparent framework; quantitative comparison still requires constrained inputs.
What we have?
experimental fitting benchmark;
validated spheroid oxygen solver;
first oxygen-to-signal bridge
virtual-experiment framework
What is still missing?
Real sample geometry,
oxygen boundary condition,
reliable optical field and normalization,
PpIX / bleaching information, instrument response, and particularly for
DLT light-to-¹O₂ source relation.
Next step
Constrain the missing inputs as independent as possible and compare the full synthetic curve with the measured curve.
Discussion: Which missing inputs can be fixed now?
Main conclusion: model the measurement first, then infer biology.
11

## Slide 12
Selected references:
-Hackbarth & Röder, Photochem. Photobiol. Sci. 14, 329–334 (2015): Heterogeneous ¹O₂ luminescence kinetics.
-Jarvi, Niedre, Patterson & Wilson, Photochem. Photobiol. 82, 1198–1210 (2006): SOLD theory and 1270-nm dosimetry challenges.
-Fernandez et al., JACS Au 6, 2627–2636 (2026): Standardized time-resolved ¹O₂ workflows and SOLIS framework.
-Foster et al., Radiat. Res. 126, 296–303 (1991): oxygen consumption and diffusion effects in PDT.
-Nichols & Foster, Phys. Med. Biol. 39, 2161–2181 (1994): Oxygen diffusion–reaction kinetics in multicellular tumour spheroids.
-Grimes et al., J. R. Soc. Interface 11, 20131124 (2014): Estimating oxygen consumption and hypoxia in tumour spheroids.
-Zhu & Liu, J. Biomed. Opt. 18, 050902 (2013): Review of MC modelling of light transport in tissues.
-Jacques, Phys. Med. Biol. 58, R37–R61 (2013): Optical properties of biological tissues.
-Wang, Jacques & Zheng, Comput. Methods Programs Biomed. 47, 131–146 (1995): MCML Monte Carlo model for multilayered tissues.
-Stepp & Stummer, Lasers Surg. Med. 50, 399–419 (2018): 5-ALA/PpIX in malignant glioma and PDT context.
12